## Slide 1: CISC 3060
Introduction to Robotics
Sensor Subsystem
.

## Slide 2: What is a sensor
A sensor is a device that the robot can query to measure something about itself or its environment.
Sensing is key for any but the simplest behaviors!

## Slide 3: Sensors
Sensors in Animals
Proprioceptive sensing
  Temperature, blood pressure, muscle contraction, chemical concentrations, etc.
Exterioceptive sensing
  Touch, sound intensity & pitch, light intensity, color, near-body motion (fish), magnetic field (birds)
We use the same taxonomy in robotics!

## Slide 4: Some common robot sensors
Internal sensing (proprioceptive)
  Wheel rotation (odometer)
  Gyroscope
  Accelerometer
  Compass and inclinometer
External sensing (exterioceptive)
  Bump sensors
  IR sensors
  Ultrasound sensors
  Laser Ranging
  Video camera
  GPS
State of the robot itself
State of the external
environment
}
}

## Slide 5: A Second Classification
Active Sensors
  Ultrasound
  Infra Red
  Radar
  Structured light (eg Microsoft Kinect)
Passive Sensors
  Camera
  Bump or limit sensors
  Gyroscope

## Slide 6: A Third Classification
Contact Sensors
  Limit or bumper switch
  Tactile sensor
Noncontact Sensor
  Camera
  Radar

## Slide 7: A Fourth Classification
Analog Sensors
  Potentiometer
  Analog camera
  Force sensor
Digital Sensor
  Bump sensor
  Limit sensor
  Digital Camera
V
Angle
V
Time
Open
Closed

## Slide 8: In Summary
A Sensor is either:
  Properioceptive or Exterioceptive
  Passive or Active
  Contact or Noncontact
  Digital or Analog

## Slide 9: General Classification (1)

## Slide 10: General Classification (2)

## Slide 11: Real Sensors
Produce noisy output signals
Return an incomplete description
Cannot be modeled completely

## Slide 12: Bump Sensors
These are ‘tactile’ or touch sensors
Typically exterioceptive, passive, contact, digital sensors.
Used to determine if the robot is in contact with the environment
Most typically a switch:
  Open when there is no contact
  Closed where there is contact

## Slide 13: Sensing of Motor Movement
Robot actuator – typically a rotary motor
Sense how much it has ‘turned’
Why? After all when you activate the motor – won’t it move as you tell it, so if you calculate by Dead Reckoning won’t you know where the robot is?
NO! Why?
It can Slip, Stall, Race, Saturate, ……
(and animal ‘muscles’ have similar issues, which is why animals have muscle sensors…)

## Slide 14: Sensing of Wheel Rotation
Two Methods:
  Resolver, Tachometer – measure velocity
  Potentiometer or encoder – measure position
Motor
Axle
Resolver
or
Encoder
Encoder is far more common - used on printers,
scanners, and other peripherals as well as robots.
Absolute Encoder: Gives a Degree reading
Incremental Encoder: Rotation relative to a start
Differential Encoder: Two readings, better accuracy
Wheel

## Slide 15: Encoder: Digital Rotation sensor
Differential digital encoder signals

## Slide 16: Odometry
The use of the wheel motion information to determine the location of the robot:
Wheel encoders can be used to measure v and w and estimate where the robot is (more later….)
BUT – what about wheel slip, wheel stall when robot is against obstacle, etc?
Use Compass and Gyroscope sensors to back up Odometry!

## Slide 17: Gyroscope
Principle: The momentum of a spinning flywheel will ‘resist’ a change in orientation
Optical Gyro: Uses optical cavity and two lasers – no moving parts

## Slide 18: Sonars
Sonar: SOund Navigation And Ranging
Sonar is a method of finding the distance to an object by measuring the time it
takes for a pulse of sound (usually ultrasound) to make the round trip back to the
transmitter after bouncing off the object (Time of Flight Measurement - TOF).
At sea level, in air, sound travels at about 344 metres per second (1130 feet per
second). In practical terms this means 2.5 cm is covered in about 74 microseconds.

## Slide 19: Sonar Beam and Arrays
VEX Sonars are pulsed
typically emit at frequency 40kHz
Range: 3cm to 3m
Example of Sonar:
Transducer cone aperture
of main lobe Is 15o for
Pioneer AT3 Sonar

## Slide 20: Sonar Issues
Sonar works best when the sensor is parallel to the target.

## Slide 21: Laser Ranging
laser
motor
encoder
Rotating mirror
Laser is scanned in plane, reflections are used to
estimate depth
Distance is estimated using a
Time-of-flight approach
Range 80m, resolution 10mm
Angular resolution 1o
Sick LM 200
Laser rangefinder

## Slide 22: Vision
Vision is a passive approach to sensing
In theory, provides a lot of information about the environment
In practice, can be difficult to interpret
1/3” Sony CCD Camera
(analog camera)
Produces images of size
640 x 480 x 3 bytes
at video frame rate
Video Frame
Grabber
Digital camera

## Slide 23: Pinhole Camera Model

## Slide 24: Issues With Vision
Each point on the image (u,v) corresponds to a point in the scene (x,y,z)
But that requires mapping 2D to 3D .. which is an underconstrained mapping.
Lighting changes dramatically alter an image (but are not changes in the elements of the scene)
Objects may be occluded, hard to recognise, hard to separate from other objects, etc.